## Slide 1: Fundamentals of LiDAR
Anjana Venkatesh 862392044
Harish Kulasekaran, 862392396
Piyush Dashpute, 862393195

## Slide 2: Introduction to LiDAR
LiDAR - Light Detection and Ranging
Remote sensing method that uses light in the form of a pulsed laser to measure distances
Notes: LiDAR – Light Detection and Ranging.
This technology, similar to radar but using light instead of radio waves, is transforming how we capture detailed 3D models of the Earth's surface.
Its applications range from environmental studies to urban planning and even in the development of autonomous vehicles.
Let's explore how this incredible technology works and its wide applications.

## Slide 3: Fundamentals of LiDAR
What is LiDAR?
  Emits laser lights to sample the earth’s surface and producing accurate 3D measurements
Key Components:
  Collection vehicle
  Laser scanner
  GPS
  INS information

## Slide 4: LiDAR Data Attributes
Data Attributes:
  Intensity
  Number of returns
  RGB
  Point Classification

## Slide 5: Types of LiDAR
Airborne
  Topographic lidar
Derive surface models
  Bathymetric lidar
Water penetrating

## Slide 6: Terrestrial LiDAR
2. Terrestrial lidar
  Mobile
Mounted on a moving vehicle
  Static
Mounted on a tripod

## Slide 7: LiDAR in Practice

## Slide 8: Storing LiDAR
LiDAR Data Attributes
  X, Y, Z, Intensity & Classification
  (X,Y) -> Location
  Z -> Elevation
  Intensity (Optional) -> Amount of light energy recorded by the sensor
  Classification (Optional) -> Type for e.g. Vegetation, Water, Ground et.,
LiDAR Intensity
  Return strength of the laser beam, depends on the reflectivity of the object
  Integer number b/w 1-256
  Uses: Feature detection and classification
Notes: Wet areas in the forest, vegetation classfication

## Slide 9: Storing LiDAR
History
  Used to measure distance b/w Apollo 15 spacecraft & Moon
  Data Format: Analog
ASCII format
LASer format
  .LAS -> Popular, supported by most LiDAR processing and GIS softwares
  X, Y, Z, Intensity, Classification Color info
  Standardized by the American Society for Photogrammetry and Remote Sensing (ASPRS)
  Compressed -> .LAZ
  Other (less popular) formats: PLY, E57
  Application specific: Autonomous cars -> Point Cloud .bin files

## Slide 10: Cloud & Database Storage for LiDAR
Popular choices
  PostgreSQL PointCloud
  Oracle Spatial
Cloud
  AWS S3, Azure Blob

## Slide 11: LiDAR Point Cloud Visualization
https://github.com/HengLan/Visualize-KITTI-Objects-in-Videos

## Slide 12: Lidar Point Classification
Lidar data points can have multiple classifications.
Flags are used for secondary descriptions.
LAS standard uses classification flags for extra point information.
These flags can be set along with the classification codes.
In LAS version 1.0 : No dual classification of attributes.
In later versions (LAS 1.1 and later), class flags were used.
These flags can be set along with the classification codes.

## Slide 13: Classification Flags
The following table describes the classification flags that can be set:
Field name | Description
Synthetic | Non-lidar point, created differently.
Key-point | Key-point exempt from thinning algorithms.
Withheld | The point should not be included in processing.
Overlap | Overlap region point between flight lines.

## Slide 14: Classification codes: LAS format 1.1 - 1.4
The following table lists the LAS classification codes defined by ASPRS for these LAS versions:
Classification value | Meaning
0 | Never classified
1 | Unassigned
2 | Ground
3 | Low Vegetation
4 | Medium Vegetation
5 | High Vegetation

## Slide 15
Thank you!
Questions?